## Slide 1
MODULE 10
Plant inspections
Each machine is a daily Yes, No or N/A.
The checklist stays locked until a competent person is selected.
A No needs a comment.
Quantum Facades · Hub training
Notes: Each machine is a daily Yes, No or N/A, signed on the pad. The person has to be marked competent on their operative record before the questions open. A No needs a comment. Open Forms, Plant Inspection.

## Slide 2
THE MACHINES
What unlocks each checklist
MCWP: the person is MCWP trained.
MEWP: the IPAF number starts with OP.
Telehandler: NPORS or CPCS on the record.
Scaffold: PASMA is Yes.
Gas torch: a Jubilee clip is a fail on every site.
Quantum Facades · Hub training
Notes: MCWP, New. Serial number and mast position. The checks open when that person is MCWP trained. On MEWP, the IPAF number has to start with OP, or they cannot be selected. Telehandler needs NPORS or CPCS on the record, or the checks stay locked. Scaffold needs PASMA Yes. Gas torch needs location, make, model and cylinder size. A Jubilee clip is a fail on every site. The public QR is the same form filled from the machine.

## Slide 3
WHEN IT GOES WRONG
They are competent and the form still locks
The card columns on their operative file are empty.
Or the training matrix does not show that ticket.
Fill IPAF, Mastclimber, PASMA, NPORS or CPCS.
Refresh name lists, and pick them again.
Quantum Facades · Hub training
Notes: If the person is competent and the form still locks, the card columns on their operative file are empty, or the training matrix does not show that ticket. Fill IPAF, Mastclimber, PASMA, NPORS or CPCS on their file, refresh name lists, and pick them again.

## Slide 4
WHEN IT GOES WRONG
Do not pick someone else just to unlock it
That puts the wrong person on a safety record.
Stop.
A No with no comment will not finish. Write what failed.
Quantum Facades · Hub training
Notes: If you select a different operative just to unlock the form, stop. That is the wrong person on a safety record. If a No is left with no comment, the form will not finish. Write what failed.