## Slide 1
MODULE 12
Flashing fabrication sheet
Five steps: material, profile, dimensions, length, review.
The picture is the section the workshop will cut.
Issue fab sheet files the PDF. Save draft does not.
Quantum Facades · Hub training
Notes: This is the workshop drawing. Five steps: material, profile, dimensions, length, review. The picture on the right is the section the folder will cut. Issue fab sheet files the PDF. Save draft does not. Open Forms, General Forms, Flashing fabrication sheet, Fill. Do not press Issue unless design wants a real sheet in the drawings folder.

## Slide 2
MATERIAL
Date, block, level, then the metal
Block is one letter, A to D.
Level is a floor number, ALL, or BM.
Material, gauge, colour and finish.
Aluminium with PPC is 2 mm minimum, Matt only, and no crushed hem.
Quantum Facades · Hub training
Notes: Set the date, block as one letter A to D, and level as a floor number, ALL, or BM. Show material, gauge, colour and finish. Switch material to Aluminium and PPC becomes available. Set PPC to Yes. The gauge drops to 2 mm and 3 mm, the crushed hem disappears, and the finish list becomes Matt only. PPC cannot be chosen on steel. Set PPC back to No and the other finishes return.

## Slide 3
PROFILE
Capping, and the two corners
Capping: 15 mm return inward at 45 degrees to downstand A.
88 degrees at A, top B, 90 degrees at C.
External and internal corners use the same section. The plan is the hand.
Plan leg 1, plan leg 2 and the joint angle appear only on a corner.
Quantum Facades · Hub training
Notes: Pick Capping. The 15 mm return kicks inward at 45 degrees to downstand A, the corner at A is 88 degrees, then top B, and the 90 degree downstand C. Pick Capping external corner, then Capping internal corner. The section is the same and the plan is the hand. On Length, Plan leg 1, Plan leg 2 and the joint angle show for a corner. Go back to a straight profile, Capping or Drip, and those three boxes are gone.

## Slide 4
REVIEW
Orange is a warning. Red means it is not ready.
Change a length and the picture and the developed width update.
Read the orange warnings.
A red line means Issue is not ready.
Quantum Facades · Hub training
Notes: On Dimensions, change one length and the picture and the developed width update. On Review, warnings are orange and errors are red. If a red line is there, the sheet is not ready.

## Slide 5
WHEN IT GOES WRONG
Block, level, part reference, or colour
Block must be one letter, A to D.
Level is a floor number, ALL, or BM.
Part reference is letters then digits, such as F-07, plus a description.
Coated steel needs a colour. Galvanised and aluminium can be left uncoloured.
Quantum Facades · Hub training
Notes: If block is rejected, it has to be one letter, A to D. If level is rejected, use a floor number, ALL, or BM. If part reference is rejected, use letters then digits, such as F-07, and a description. Coated steel needs a RAL or BS colour. Galvanised and aluminium can be left uncoloured. Mill finish and no colour do not mark a colour face.

## Slide 6
WHEN IT GOES WRONG
Aluminium and PPC, the coil, or an order already placed
No 0.7 mm, no crushed hem, no Satin. Use 2 mm or 3 mm, Matt.
A developed-width warning may mean it will not fit the coil. Do not ignore it.
If a purchase order covers this sheet, Save and Delete are blocked.
Speak to procurement before you expect the order to change.
Quantum Facades · Hub training
Notes: Aluminium and PPC will not offer 0.7 mm, a crushed hem, or Satin. That is deliberate. Use 2 mm or 3 mm, no hem, Matt. If the developed width warns it may not fit the coil, read the warning to the workshop. Do not ignore it and issue. If the status says a purchase order covers this sheet, Save and Delete are blocked. The PDF still opens. You cannot quietly change a sheet that has already been ordered. Speak to procurement before you expect the order to change. If the page still shows yesterday’s profile, refresh. Not saved yet means you have not pressed Save draft.